## Slide 1: Computation II
5EIB0
Instruction Set Architecture
(ISA)
Henk Corporaal
February 2016
MIPS_3000

## Slide 2: What do you learn today?
RECAP of MIPS ISA:
Basic instruction set of any computer
Machine code (format, structure)
Important RISC principles
Addressing modes
How to translate C into Assembly code
Use of SPIM simulator
Book: Patterson&Hennessy Computer Organization, 5th ed
  study chapter 2.1-2.11, extra reading 2.12-2.14
  (NOTE: 4th ed: 2.1-2.11, reading 2.12-2.14)

## Slide 3
Trends:
#transistors follows Moore
but not freq. and performance/core
Core i7
3GHz
100W
5
Crisis?

## Slide 4: Conceptual structure of a computer system; How does it operate?
Instruction
memory
Data
memory
I/O
interfaces
Input and output
devices
Processor

## Slide 5: What’s inside the processor? E.g., Pipelined MIPS
PC

## Slide 6: How does this pipeline operate?
let's take a load instruction at address 0x800:
  0x800 lw $s1, 8($s2)
Every instruction passes 5 stages (= 5 cycles):
Cycle 1
  Fetch instruction to which PC (Program Counter) points
  New PC = PC+4
Cycle 2
  Decode instruction
  Fetch $s2 from register file
Cycle 3
  Execution: Add 8 to $s2
Cycle 4
  Fetch data from address (8+$s2)
Cycle 5
  Write data back to register file location $s1

## Slide 7: Types of Instructions of any Computer
Basically we need only 3 types of instructins/operations:
Arithmetic
  Integer
  Floating Point
Memory access
  Load & Store
Control flow
  Jump
  Conditional Branch
  Call & Return

## Slide 8: MIPS arithmetic
C code: A = B + C + D; E = F - A; MIPS code: add $t0, $s1, $s2 add $s0, $t0, $s3 sub $s4, $s5, $s0
Operands must be registers,
Only 32 registers provided, why not more?
Design Principle: smaller is faster. Why?

## Slide 9: Registers vs. Memory
Operands of arithmetic instructions must be registers
  MIPS has 32 (integer) registers
  Compiler associates variables with registers
Question: What about programs with >32 of variables ?
CPU
Memory
IO
register file
32 registers

## Slide 10: Instructions: Load and store
Example: C code: A[8] = h + A[8]; MIPS code: lw $t0, 32($s3) add $t0, $s2, $t0 sw $t0, 32($s3)
Store word operation has no destination (reg) operand
Remember: on a RISC processor arithmetic operands are registers, not memory!

## Slide 11: Machine Language: Arithmetic
Instructions are also 32 bits long
  Example: add $t0, $s1, $s2
  Registers have numbers: $t0=9, $s1=17, $s2=18
Instruction Format (R-type):
Question: Can you guess what the field names stand for?
6 bits
5 bits
5 bits
5 bits
6 bits
5 bits
000000 10001 10010 01001 00000 100000
op rs rt rd shamt funct

## Slide 12: Machine Language: Load & Store
Example: lw $t0, 32($s2)
Introduce a new type of instruction format: I-type
35 18 9 32
op rs rt 16 bit number
Question: Where's the compromise?

## Slide 13: Control
Decision making instructions
  alter the control flow,
  i.e., change the "next" instruction to be executed
MIPS conditional branch instructions: bne $t0, $t1, Label beq $t0, $t1, Label
Example: if (i==j) h = i + j; bne $s0, $s1, Label add $s3, $s0, $s1 Label: ....

## Slide 14: Control
MIPS unconditional branch instructions: j label
Example: if (i!=j) beq $s4, $s5, Lab1 h=i+j; add $s3, $s4, $s5 else j Lab2 h=i-j; Lab1: sub $s3, $s4, $s5 Lab2: ...

## Slide 15: So far:
Instruction Meaning
add $s1,$s2,$s3 $s1 = $s2 + $s3 sub $s1,$s2,$s3 $s1 = $s2 – $s3 lw $s1,100($s2) $s1 = Memory[$s2+100] sw $s1,100($s2) Memory[$s2+100] = $s1 bne $s4,$s5,L Next instr. is at Label if $s4 ≠ $s5 beq $s4,$s5,L Next instr. is at Label if $s4 = $s5 j Label Next instr. is at Label
Formats:
op rs rt rd shamt funct
op rs rt 16 bit address
op 26 bit address
R
I
J

## Slide 16: MIPS compiler conventions

## Slide 17: Constants
50% of operands are small constants !! e.g., A = A + 5; B = B + 1; C = C - 18;
How to support them?
  put 'typical constants' in memory and load them?
  create hard-wired registers (like $zero) for small constants?
  . . . ???
MIPS Instructions: addi $29, $29, 4 slti $8, $18, 10 andi $29, $29, 6 ori $29, $29, 4

## Slide 18: How to construct larger constants?
Must use two instructions to construct any 32-bit number; new "load upper immediate" instruction:
lui $t0, 1010101010101010
1010101010101010
0000000000000000
0000000000000000
1010101010101010
1010101010101010
1010101010101010
ori
1010101010101010
0000000000000000
filled with zeros
Then must get the lower order bits right, i.e., ori $t0, $t0, 1010101010101010

## Slide 19: Addresses in Branches and Jumps
Instructions:
  bne $t4,$t5,Label Next instruction is at Label if $t4  $t5
  beq $t4,$t5,Label Next instruction is at Label if $t4 = $t5
  j Label Next instruction is at Label
Formats:
Questions: Above addresses are not 32 bits; they are 16 & 26 bits !!
  How do we extend them to 32 bits?
op
op
rs
rt
16 bit address
26 bit address
I
J

## Slide 20: Addresses in Branches and Jumps
Instructions:
  bne $t4,$t5,Label Next instruction is at Label if $t4  $t5
  beq $t4,$t5,Label Next instruction is at Label if $t4 = $t5
  j Label Next instruction is at Label
Branch
  PC_next = PC_branch + 4 + ( Instr[15..0] || [00] ), or
  PC_next = PC_branch + 4 + 4*Label
Jump: use high order (4) bits of PC
  32-bit Jump address = PC[31..28] || Instr[25..0] || [00]
  Address boundaries of 256 MB
Questions:
  Why do we concat 2 zero’s for instruction addresses?
  Why don’t we do this for data memory addresses?
Concatenating bits

## Slide 21: MIPS has (only) 3 data addressing modes
data operands
next instruction address

## Slide 22: To summarize:

## Slide 23: More complex:
Inequalities
While statement
Procedure / Function
  leaf
  non-leaf / recursive
Stack usage
Further (study your book for these ones)
  Case/Switch statement
  Arrays vs Pointers
  Strings and String Copy

## Slide 24: Inequalities
We have: beq, bne, what about Branch-if-less-than?
New (arithmetic) instruction needed:
slt $t0, $s1, $s2 // $t0 = 1 if $s1<Ss2, else 0
Can use this to build a ‘blt’ pseudo instruction e.g.:
blt $s1, $s2, Label
  you can now build all general control structures !!
Question: What is a pseudo instruction?

## Slide 25: While statement
while (save[i] == k)
i=i+j;
Loop: muli $t1,$s3,4
add $t1,$t1,$s6
lw $t0,0($t1)
bne $t0,$s5,Exit
add $s3,$s3,$s4
j Loop
Exit:
# calculate address of
# save[i]
Registers allocation:
i $s3
base of save[] $s6
k $s5
sll $t1,$s3,2
Faster alternative

## Slide 26: Function call / return
Function call
  jal label
  jump to label (i.e. starting address of the callee),
  and make $ra = PC+4
Function return
  jr $ra
  new PC = $ra
Return address (ra)
is kept in $ra = r31 on MIPS

## Slide 27: Using a Stack
$sp
low address
high address
filled
empty
Save $s0 and $s1:
subi $sp,$sp,8
sw $s0,4($sp)
sw $s1,0($sp)
Restore $s0 and $s1:
lw $s0,4($sp)
lw $s1,0($sp)
addi $sp,$sp,8
Convention: $ti registers do not have to be saved and restored by callee;
They are scratch registers
Question: Who takes care when changing $ti registers?

## Slide 28: Compiling a leaf procedure / function
C code
int leaf_example (int g, int h, int i, int j)
{
int f;
f = (g+h)-(i+j);
return f;
}
Assembly code:
leaf_example: - save $si registers changed by callee
- code for expression ‘f = ....’
(g is in $a0, h in $a1, etc.)
- put return value in $v0
- restore saved registers
- return: jr $ra

## Slide 29: Let’s simulate: SPIM
Install PCSpim
  http://spimsimulator.sourceforge.net/
Documentation
  book: appendix B.9
  www.cs.wisc.edu/~larus/SPIM/spim_documentation.pdf

## Slide 30: SPIM in action
MIPS registers
Program memory
Data memory
Messages

## Slide 31: SPIM example 1: add two numbers
# $t2 - used to hold the sum of the $t0 and $t1.
# $v0 - syscall number, and syscall return value.
# $a0 - syscall input parameter.
.text # Code area starts here
main:
li $v0, 5 # read number into $v0
syscall # make the syscall read_int
move $t0, $v0 # move the number read into $t0
li $v0, 5 # read second number into $v0
syscall # make the syscall read_int
move $t1, $v0 # move the number read into $t1
add $t2, $t0, $t1
move $a0, $t2 # move the number to print into $a0
li $v0, 1 # load syscall print_int into $v0
syscall #
li $v0, 10 # syscall code 10 is for exit
syscall #
# end of main
Assembler directive
starts with a dot
Special SPIM
instruction: system call

## Slide 32: SPIM/MIPS assembly directives
.data start data segment
.ascii str store the string str in memory without '\0'
.asciiz str idem, with '\0'
.byte 3,4,16 store 3 byte values
.double 3.14, 2.72 store 2 doubles
.float 3.14, 2.72 store 2 floats
.word 3,4,16 store 3 32-bit quantities
.space 100 reserve 100 bytes
.text start text segment

## Slide 33: SPIM syscall examples
Service | Trap code | Input | Output
print_int | $v0 = 1 | $a0 = integer to print | prints $a0 to standard output
print_float | $v0 = 2 | $f12 = float to print | prints $f12 to standard output
print_double | $v0 = 3 | $f12 = double to print | prints $f12 to standard output
print_string | $v0 = 4 | $a0 = address of first character | prints a character string to standard output
read_int | $v0 = 5 |  | integer read from standard input placed in $v0
read_float | $v0 = 6 |  | float read from standard input placed in $f0
read_double | $v0 = 7 |  | double read from standard input placed in $f0
read_string | $v0 = 8 | $a0 = address to place string, $a1 = max string length | reads standard input into address in $a0
sbrk | $v0 = 9 | $a0 = number of bytes required | $v0= address of allocated memory Allocates memory from the heap
exit | $v0 = 10 |  | 
print_char | $v0 = 11 | $a0 = character (low 8 bits) | 
read_char | $v0 = 12 |  | $v0 = character (no line feed) echoed
file_open | $v0 = 13 | $a0 = full path (zero terminated string with no line feed), $a1 = flags, $a2 = UNIX octal file mode (0644 for rw-r--r--) | $v0 = file descriptor
file_read | $v0 = 14 | $a0 = file descriptor, $a1 = buffer address, $a2 = amount to read in bytes | $v0 = amount of data in buffer from file (-1 = error, 0 = end of file)
file_write | $v0 = 15 | $a0 = file descriptor, $a1 = buffer address, $a2 = amount to write in bytes | $v0 = amount of data in buffer to file (-1 = error, 0 = end of file)
file_close | $v0 = 16 | $a0 = file descriptor | 

## Slide 34: SPIM example 2: sum N numbers
Input:
  number of inputs, n,
  n integers;
  Query the user for these n+1 numbers; first put message on output display
Output: Sum of integers
  display this sum

## Slide 35: SPIM example 2: sum N numbers
# Input: number of inputs, n, and n integers; Output: Sum of integers
.data # Data memory area.
prmpt1: .asciiz "How many inputs? "
prmpt2: .asciiz "Next input: "
sumtext: .asciiz "The sum is "
.text # Code area starts here
main: li $v0, 4 # Syscall to print prompt string
la $a0, prmpt1 # li and la are pseudo instr.
syscall
li $v0, 5 # Syscall to read an integer
syscall
move $t0, $v0 # n stored in $t0
li $t1, 0 # sum will be stored in $t1
while: blez $t0, endwhile # (pseudo instruction)
li $v0, 4 # syscal to print string
la $a0, prmpt2
syscall
li $v0, 5
syscall
add $t1, $t1, $v0 # Increase sum by new input
sub $t0, $t0, 1 # Decrement n
j while
endwhile: li $v0, 4 # syscal to print string
la $a0, sumtext
syscall
move $a0, $t1 # Syscall to print an integer
li $v0, 1
syscall
li $v0, 10 # Syscall to exit
syscall

## Slide 36: Exercise 1: For Loop
Translate the following C-loop into MIPS assembly code. For variables x and y use registers $5 and $6 respectively.
Test it out with SPIM
int x, y;
for (x=0, y=100; x != y; x++, y--) ;

## Slide 37: Exercise 2: Sum N numbers
Input:
  number of inputs, n,
  n integers;
  Query the user for these n+1 numbers; first put message on output display
Output: Sum of integers
  display this sum
Again: test it out with SPIM

## Slide 38: What did you learn so far?

## Slide 39
3 Types of instructions:
  Arithm., Data access, Control
3 Instruction formats: R, I, J
Main MIPS instructions
Compiler conventions about register use
Addressing modes
Some RISC principles
  Supply lots of registers
    avoid unnecessary loads and stores
  Arithmetic instructions may only use register operands
  Few instruction formats
    easy to decode
  Few operand addressing modes
  Only 1 instruction length (32 bits)
With bne, beq, j and slt you can code any loop and if-statement
Use of SPIM

## Slide 40: FurtherTopics
Study the book for the following related topics:
  compiling non-leaf procedure / function
  register allocation using graph coloring
  alignment of data
  floating point instructions
  characters and strings
  string copy code
  case statement